## Slide 1: Remote Sensing and Rasters!
November 20, 2018

## Slide 2
Notes: When light is released from its source—let’s say our sun—and interacts with an object, there are a number of things can happen to the light waves. Three of the most common are: reflection, transmission, and absorption.
Reflection: Light bounces off an object.
Absorption: Light particles interact with the particles in an object, causing them to vibrate. What do you think happens when the object’s atoms vibrate a lot? The object gets hot! So, the object gives off heat/thermal energy in the infrared wavelength. What kind of object absorbs the most heat? What color do you not wear on a hot and sunny day? That’s because dark bodies absorb solar radiation!
Transmission: Light passes through the object without being disturbed. Certain wavelengths of light can pass through clouds and other particles in our atmosphere.
Images from https://science.nasa.gov/ems/03_behaviors.

## Slide 3
Reflectance Spectra
Notes: Every object has something called a reflectance spectrum. It shows the wavelengths of light that are reflected and absorbed by the object.
What do you notice about this chart? It shows the reflectance curve of butter (A), tomato (B), and lettuce (C)
What’s the takeaway here? Objects don’t “have” color—they reflect light that appears as a certain color to our eyes!
(note: every individual object has a slightly different spectrum, so if you have a sensor with high enough resolution you can detect individual plant species just based on an image!)

## Slide 4
What can light tell us about the Earth’s environment and surface features?
Notes: So, we talked about the source of different kinds of light and the different ways that light can interact with an object. But what can light tell us about the environment and the features on the Earth’s surface?
That’s great! We can see features like soil, snow, vegetation, and surface temperature based on how light waves interact with those objects and features on the earth’s surface or its interior.
Does anyone have any ideas about how we make these measurements? What kind of tools can we use?
Yes! One way that scientists and researchers do that is with satellites!
(A camera/photo captures light values, but only for the visible spectrum. A satellite can record those values and then use a computer to convert that information digitally into a color image.)

## Slide 5
Notes: What do you see in this image? Can you tell from the image why healthy plants are generally green?
In a healthy leaf, the pigments reflect green near-infrared light and absorb red and blue light.
How could we tell from a reflectance spectrum whether we are looking at a plant or some other feature, like a lake? What wavelengths should we look for?
How do you think an autumn leaf’s reflectance spectrum would differ from a green leaf’s?
Visible and near-infrared light reflections can be used to measure properties of vegetation and soil.

## Slide 6
Notes: The leaf’s visible color is completely attributed to that little spike in the visible section of the graph. In this case it’s in the orange-red color range!

## Slide 7: What is raster data?
Notes: Raster or "gridded" data are stored as a grid of values which are rendered on a map as pixels. Each pixel value represents an area on the Earth's surface.

## Slide 9: What kind of info is stored in a raster?
Classified
Landcover/land use maps
Tree height maps classified as short, medium, tall trees
Elevation maps classified as low, medium, tall trees
Continuous
Precipitation maps
Maps of tree height (from LiDAR data) [UV, visible, IR light]
Elevation values (DEM)
Notes: Raster data can be continuous or categorical. Continuous rasters can have a range of quantitative values. Some examples of continuous rasters include:
LiDAR = light detection + ranging
DEM = digital elevation model
Some rasters contain categorical data where each pixel represents a discrete class such as a landcover type (e.g., "forest" or "grassland") rather than a continuous value such as elevation or temperature.

## Slide 10: Classified: land cover map
Notes: Raster or "gridded" data are data that are saved in pixels. In the spatial world, each pixel represents an area on the Earth's surface. For example in the raster below, each pixel represents a particular land cover class that would be found in that location in the real world.

## Slide 11: Continuous: DEM (digital elevation model)

## Slide 12: Spatial Resolution
https://www.neonscience.org/primer-raster-data-r
Notes: A raster consists of a series of pixels, each with the same dimensions and shape. In the case of rasters derived from airborne sensors, each pixel represents an area of space on the Earth's surface. The size of the area on the surface that each pixel covers is known as the spatial resolution of the image. For instance, an image that has a 1 m spatial resolution means that each pixel in the image represents a 1 m x 1 m area.

## Slide 15: Spatial Extent
Notes: The spatial extent of a raster, represents the "X, Y" coordinates of the corners of the raster in geographic space. This information, in addition to the cell size or spatial resolution, tells the program how to place or render each pixel in 2 dimensional space. Tools like R, using supporting packages such as rgdal and associated raster tools have functions that allow you to view and define the extent of a new raster.

## Slide 16: NoData Values
In this image, the black edges have been assigned NoDataValue. R doesn't render pixels that contain a specified NoDataValue. R assigns missing data with the NoDataValue as NA.
https://www.neonscience.org/dc-raster-data-r
Notes: Raster data often has a NoDataValue associated with it. This is a value assigned to pixels where data are missing or no data were collected.
By default the shape of a raster is always square or rectangular. So if we have a dataset that has a shape that isn't square or rectangular, some pixels at the edge of the raster will have NoDataValues. This often happens when the data were collected by an airplane which only flew over some part of a defined region.
In the image below, the pixels that are black have NoDataValues. The camera did not collect data in these areas.

## Slide 17: Bad Data Values in Rasters
Bad data values are different from NoDataValues. Bad data values are values that fall outside of the applicable range of a dataset.
Examples of Bad Data Values:
The normalized difference vegetation index (NDVI), which is a measure of greenness, has a valid range of -1 to 1. Any value outside of that range would be considered a "bad" or miscalculated value.
Reflectance data in an image will often range from 0-1 or 0-10,000 depending upon how the data are scaled. Thus a value greater than 1 or greater than 10,000 is likely caused by an error in either data collection or processing.
Notes: Sometimes a raster's metadata will tell us the range of expected values for a raster. Values outside of this range are suspect and we need to consider than when we analyze the data. Sometimes, we need to use some common sense and scientific insight as we examine the data - just as we would for field data to identify questionable values.
From: https://www.neonscience.org/dc-raster-data-r

## Slide 18: Raster Bands
Notes: The Digital Surface Model object (DSM_HARV) that we've been working with is a single band raster. This means that there is only one dataset stored in the raster: surface elevation in meters for one time period.